## Slide 1: Real World Evaporative Emissions Studies
22nd CRC Real World Emissions Workshop
March 2012
Constance Hart
David Hawkins

## Slide 2: Acknowledgments
High Evaporative Emission Field Studies:
  Constance Hart, Carl Fulper, David Hawkins, James Warila, David Brzezinski, US EPA
  James Kemper, James Sidbottom, Colorado Department of Public Health and Environment (CDPHE)
  Sandeep Kishan, Michael Sabisch, Jim Lindner, Timothy DeFries, Eastern Research Group (ERG)
Evaporative OBD Analysis:
  Constance Hart, Carl Fulper, Arvon Mitcham, Antonio Fernandez, Glenn Passavant, US EPA
  Sandeep Kishan, Michael Sabisch, Meridith Weatherby, Cindy Palacios, Timothy DeFries, Jim Lindner, ERG
Multi-Day Diurnal Testing
  Constance Hart, David Hawkins, Jarrod Brown, US EPA
  Jim Lindner, Sandeep Kishan, ERG
  Gerard Glinsky, Environmental Testing Corporation (ETC), SGS
  Michael St. Denis, Joseph Roeshen, Revcorp

## Slide 3: Real World Evaporative Emissions Studies
Three years of High Evap Field Studies
  Presented at 19th CRC Emissions Workshop 2009
  RSD usefulness as a screening tool
  Portable SHED and other tools
Current and Future Work
  Evap OBD
  Multi-day diurnal testing

## Slide 4: High Evaporative Emissions Field Studies in Denver, CO
Lipan IM Station, 2008
Ken Caryl IM Station, 2009
Repair Effectiveness, 2010
Handheld HC detector
Portable SHED set up in IM Station

## Slide 5: Is RSD a reliable tool for evaporative emission screening?
Found RSD to be useful for detecting gross emitting evaporative emissions
Important for Inventory
Still evaluating the newer vehicles
“Custom” Sound System Attachment Points

## Slide 6: Portable SHED and Other Tools
PSHED was very effective means for testing large amounts of vehicles in the field
  Average Recovery 97.6%
  Average Retention 95.7%
  Significant savings over laboratory SHED testing
Handheld HC Detector
  Effective when can reach the source of emissions
  Many newer vehicles packed very tightly, difficult to reach to determine the source without dropping tank and fuel lines
Snap-On device for leak detection
  Can determine if leak in system and cumulative size

## Slide 7: High Evap Studies 1996+ OBD Equipped Vehicles
Field study sampled in bins, ~1/2 vehicles in first two summers and most of 2010 study were “high”, > 1.0 g/Qhr:
  1.0 g/Qhr ~ 0.020” diameter leak in E-77 programs
  ~ lowest range which evaporative emissions could be detected by RSD monitors, getting into noise of instrument
Many of the high values are older vehicles, but there were some in the 1996+ range.
  157 OBD equipped vehicles

## Slide 8
High Evap Studies 1996+ OBD Equipped Vehicle Pairs
Vehicles with Evaporative DTCs Set

## Slide 9: Evap OBD vs High PSHED Measurements for “ready” vehicles
Out of 20 - only 10 are expected to be identified by OBD
Only 3 of the 10 vehicles had Evap DTCs set with
high SHED values
50-70% of high SHED values were not picked up by OBD when the vehicles were designed to (10 vehicles)

## Slide 10
Model Year | SHED g/15 min | Evap DTC | Evap Monitor Ready | Should it be detectable by OBD?
2002 | 1.30 | No | Y | ?
1998 | 2.10 | No | Y | ?
1999 | 2.18 | No | N | ?
2000 | 2.45 | No | N | Yes
1998 | 6.30 | No | Y | Yes
1998 | 11.22 | No | Y | ?
1997 | 20.81 | No | Y | Yes – purge solenoid
2002 | 5.21 | Yes | Y | Yes
1996 | 12.21 | Yes | Y | Yes – purge solenoid
1998 | 19.93 | Yes | Y | Yes – purge solenoid
PSHEDs > 1.0 g/15 min for Vapor
(excluding liquid and unmonitored vapor leaks)

## Slide 11: 14-day Diurnal Testing
Notes: First program to have the on vehicle canister weight

## Slide 12: Multi-Day Diurnal Testing
Developed test procedure to monitor evaporative emissions, canister loading profiles and breakthrough emissions
Tested 9 vehicles at Environmental Testing Corporation (ETC, now a part of SGS), Summer 2011
14 days of Federal Diurnal Cycle 72o – 96oF
Each vehicle tested on 2 fuels:
  Represent 9.0 RVP at Sea Level, used 8.0 in Denver
  Represent 10.0 RVP at Sea Level, used 9.0 in Denver

## Slide 13: Vehicles
Make | Model | Model Year | Odometer | Canister Working Capacity (g) | Tank Volume (gal)
Subaru | Legacy | 2010 | 17,237 | 144 | 18.5
Saturn | Outlook | 2009 | 120,403 | 197 | 22
Toyota | Camry | 2009 | 121,187 | 130 | 18.5
Ford | Focus | 2009 | 120,785 | 125 | 13.5
Chevrolet | Silverado | 2006 | 109,954 | 176 | 32.4
Nissan | Altima | 2008 | 123,261 | 120 | 20
Ford | Focus | 2010 | 28,390 | 110 | 14.5
Ford | Taurus | 2008 | 115,599 | 145 | 20
Toyota | Prius | 2010 | 27,289 | 110 | 119

## Slide 14: Test Procedure
Drain and Refuel
6-36 Hour Soak
Precondition - 3 Phase FTP With Hot Soak
Drain and Refuel
Canister Load to 2 Gram Breakthrough
Emissions Test - 3 Phase FTP With Hot Soak
Vehicle Soak Cool Down
14 Day VT SHED

## Slide 15
SHED Schematic

## Slide 16
Outside Canister, “9”RVP
Outside Canister, “10”RVP
Vehicle Canister, “10” RVP
Vehicle Canister, “9” RVP
Breakthrough

## Slide 17
PZEV Vehicle
Breakthrough
?

## Slide 18
Bleed?

## Slide 19: ETC Enhanced Test Procedure

## Slide 20
14 Day VT SHED - RVP 10 Fuel
SGS Saturn Outlook
Early HC slip

## Slide 21
14 Day VT SHED - RVP 10 Fuel
SGS Ford Focus

## Slide 22: Conclusions
Field studies found RSD useful for detecting gross emitting evaporative emissions – important for inventory
OBD analyses valuable – still assessing ability to catch “high evap”
Multi-day testing gives us better understanding of vehicle canister loading/purging cycling
  Backpurge is very different than our initial estimate which was based on limited marine data.
  ETC’s revised procedure more accurate, confirms our 9 vehicle program data